## Slide 1: Optimization for CPU Inference (Chapter 4)
Oliver Grainge

## Slide 2: Learning Outcomes
By the end of this session, you will know how to:
  Apply algorithmic optimizations for CPU inference, including:
    Linear quantization
    Network pruning.
  Optimize matrix multiplication through:
    Loop tiling
    Loop reordering
    Loop unrolling
    Multithreading.
  Leverage Arm CPU SIMD technologies for faster inference:
    Neon
    Scalable Vector Extension (SVE)
    Int8 matrix multiply (I8MM)
    Scalable matrix extension (SME).
  Combine these methods with the Kleidi micro-kernel to maximize performance.
Notes: Overview of the session's goals for optimizing CPU inference.
Algorithmic optimizations: linear quantization and network pruning.
Matrix multiplication optimizations: loop tiling, reordering, unrolling, and multithreading.
SIMD acceleration techniques using Arm CPU features like Neon, SVE, and I8MM for increased data parallelism
Combining these techniques with Kleidi micro-kernel a low-level operator library for maximum performance.

## Slide 3: Linear Quantization
Linear Quantization maps floating-point range to quantized range with an optional offset.
Quantization:
Dequantization:
Floating Point Range
Floating-point
Integer
Notes: Converts floating point values to a quantized range for efficiency.
Scale factor (S) determines mapping between floating-point and integer values.
Zero-point (Z) accounts for offset in quantized representation.
Clipping and rounding ensure values remain in the valid range.
Dequantization reverses the process for approximate floating-point recovery.

## Slide 4: Data Formats on ARM
  Data Formats (fp32 -> fp16/bfp16 -> int8 -> int4)
    Reduces the bit width of parameters to lower memory and compute cost.
    Reducing bit-widths reduces numerical precision (the number of representable values).
    Bf16 has higher dynamic range compared to fp16, and avoids overflow errors.
int4
int8
fp16
fp32
  Sign bits
  Exponent bits
  Mantissa bits
  Value bits
bf16
Notes: Different numerical formats: fp32, fp16, bf16, int8, and int4.
Lower bit-widths reduce memory and computational cost.
Trade-off: reduced numerical precision for efficiency gains.
bfloat16 (bf16) has a higher dynamic range than fp16, preventing overflow errors.
Integer representations optimize performance in low-precision inference.

## Slide 5: Neural Network Pruning
Han, S., Pool, J., Tran, J and Dally, W. (2015, December 7–12). Learning Both Weights and Connections for Efficient Neural Network [Conference Paper] Neural Information Processing Systems, Montreal, Canada. https://doi.org/10.48550/arXiv.1506.02626
Pruning removes redundant weights, neurons or activations from the network.
High level of unstructured sparsity can be achieved with minimal accuracy loss
A common approach, iterative magnitude pruning:
Dense Network
Pruned Network
Neuron Pruning
Connection Pruning
Train a Dense Network
Remove smallest p% of weights
Fine-tune
Output Pruned Network
Notes: Removes redundant neurons, weights, or activations to improve efficiency.
Unstructured sparsity minimizes accuracy loss while reducing compute.
Iterative magnitude pruning: gradually removing the lowest-magnitude weights.
Fine-tuning ensures the network maintains performance after pruning.
Different pruning strategies: neuron pruning vs. connection pruning.

## Slide 6: Implementation Optimization: Loop Reordering
Naive matrix multiplication loops can be reordered.
  The ordering affects memory access pattern.
  Loop reordering improves access pattern in A and B
Naive Matrix Multiplication
Row Access = A[6:12]
Column Access = A[0], A[7], A[13], …
When Matrices are stored in Row-Major order
Loop reordered Matrix Multiplication
Notes: Improves memory access patterns in matrix multiplication.
Standard naive matrix multiplication follows an inefficient access pattern.
Row-major storage affects how data is accessed in memory.
Reordering loops (ijk → ikj) improves data locality and reduces cache misses.
Significant speed-up in large matrix multiplications.

## Slide 7: Implementation Optimization: Tiling
Matrix multiplication is an extremely parallelizable operation.
Matrices of GenAI models are huge!
  Can be N >> 1024.
Main memory access slow, cache is fast.
  Global DRAM is much slower than on-chip caches.
Reducing global memory access, speeds up inference.
  Tiling reuses rows/columns in cache, boosting performance.
  Increases ops/DRAM memory access ratio.
Naive matrix multiplication
Tiled matrix multiplication
Notes: Matrix multiplication is highly parallelizable but memory-bound.
DRAM access is slow compared to on-chip cache.
Tiling partitions matrices into smaller blocks to fit within cache.
Reusing data in cache improves efficiency and reduces DRAM bottlenecks.
Results in higher ops/memory access ratio and improved inference speed.

## Slide 8: Implementation Optimization: Loop Unrolling
Matrix Multiplications provide branching overhead.
  Have to evaluate:
    i < N
    j < N
    k < N.
Reduces branching overhead.
Better Instruction scheduling.
  Exposing more independent operations, allows CPU to schedule parallel pipelines.
Reduced branch misprediction penalties.
Naive matrix multiplication
Naive matrix multiplication
Notes: Matrix multiplications introduce branching overhead due to loop evaluations.
Unrolling loops reduces branching overhead, improving execution speed.
Allows better instruction scheduling by exposing more independent operations.
Reduces branch misprediction penalties, minimizing performance stalls.
Example shows unrolling by a factor of four, processing multiple iterations in one step.

## Slide 9: Multi-Core Parallel Programming on ARM
Matrix multiplication is highly parallelizable.
  It can exploit multiple cores or threads simultaneously for faster execution.
Multithreading boosts throughput.
  Different parts of the matrix multiplication can run on separate threads or cores.
Modern Arm and Cloud processors often support simultaneous multithreading (SMT).
  This allows more than one thread of execution per core, further increasing parallelism.
Parallelized Naive Matrix Multiplication
Notes: Matrix multiplication is highly parallelizable and benefits from multi-core execution.
Multithreading allows different parts of the matrix to be processed simultaneously.
Arm and Cloud processors support simultaneous multithreading (SMT) for increased parallelism.
OpenMP is a common tool for parallelizing loops efficiently.
Code example illustrates how to parallelize the outer loop using OpenMP.

## Slide 10: Overview of Arm’s SIMD Capabilities
Single instruction multiple data (SIMD)
  Performs the same operation on multiple data elements concurrently
  Increases throughput for matrix multiplication
  Arm’s advanced implementation of SIMD instructions is the Neon feature.
Arm advanced SIMD features:
  Scalable Vector Extension
    Increased vectorization and enhanced throughput.
    Introduces vector-length agnostic approach.
  I8MM
    Feature of Arm Processors to accelerate integer matrix multiply.
    Specifically suited for INT8 quantized networks.
    Multiplies 2x8, 8x2 matrix segments to output 2x2 results.
  SME
    Builds on Neon to use 2D vectorization
    Specifically developed for matrix multiply operations.
    Extends SVE concepts by adding dedicated instructions for matrix-based computations.
  Neon Vector Multiplication
Notes: SIMD (Single Instruction Multiple Data) executes the same operation on multiple elements in parallel.
Neon is ARM’s SIMD implementation for vectorized operations.
Scalable Vector Extension (SVE) improves vectorization by supporting variable-length registers.
I8MM accelerates integer matrix multiplication, useful for quantized models.
SME (Scalable Matrix Extension) builds on Neon and SVE for 2D vectorization.

## Slide 11: I8MM: Accelerated Int8 Matrix Multiplication
Quantization can reduce precision to INT8
I8MM designed to specifically accelerate INT8 matrix multiplication.
  SMMLA (vector) instruction will deliver a peak integer multiply throughput that is at least as high as can be achieved using two SDOT (vector) instructions
  Mandatory features of Armv8.6+
SMMLA <Vd>.4S, <Vn>.16B, <Vm>.16B
  <Vd> the destination register
  <Vn> is the first source register
  <Vm> the second source register
Notes: Quantization reduces precision to INT8, improving efficiency.
I8MM accelerates INT8 matrix multiplication with specific hardware instructions.
SMLA vector instruction delivers peak integer multiply throughput.
Mandatory feature for Armv8.6+ architecture.

## Slide 12: Scalable Vector Extension (SVE)
No fixed width (unlike Neon) – the same code can scale from 128 to 2048 bits.
Vector length must be a power of two (
Guarantees, same implementation can run on different widths of SVE
SVE Registers (Z0–Z31) shared with Neon (last 128 bits)
Predicate Registers (P0–P7) provide fine-grained control over which elements in the vector are active.
SVE Registers (Z0–Z31)
Predicate Registers (P0–P7)
Notes: Unlike Neon, SVE implementations can scale from 128 to 2048 bits, making it more flexible.
Vector length design implementations must be a power of two, ensuring compatibility.
Code using SVE can run on different vector widths without modification.
Registers Z0–Z31 are shared with Neon for compatibility.
Predicate Registers (P0–P7) allow fine-grained control over vector execution.

## Slide 13: Scalable Matrix Extension (SME)
An extension to SVE to operate on matrix tiles.
Streaming SVE mode adds new instructions specifically for matrix multiplication.
Dedicated matrix tile storage (ZA) array
  Just like SVE, SME has variable length tile vector storage (SVL).
Matrix tile storage (ZA Array)
Dedicated matrix tile storage (ZA) array
  As SVE has a variable length vector (SVL).
  SME has variable length tile vector storage (SVL).
SME New instructions
  Outer Product () operations.
  Load/Store and Transposition.
  Additional Arithmetic and Logical Operations (e.g. zeroing tiles).
ZA Array memory access
  ZAOH.B[n] accesses the nth row
  ZAOV.B[n] accesses the nth column
Notes: SME extends SVE to operate on matrix tiles, improving efficiency.
Streaming SVE mode introduces new instructions for optimized matrix multiplication.
Dedicated ZA matrix storage allows for more efficient tile-based computation.
ZA storage supports row and column accesses, optimizing memory layout.
New SME instructions include outer product operations, transposition, and logical operations.

## Slide 14: What We Have Covered So Far
Algorithmic Optimizations
  Quantization (e.g., INT8) for faster compute
  Pruning to reduce computation & memory footprint
Implementation Optimizations
  Loop tiling and blocking for cache locality
  Loop reordering for improved memory access pattern
  Loop unrolling for reduced overhead
  Multithreading for core-level parallelism
ARM Architecture Features
  Neon (SIMD)
  SVE (Scalable Vector Extension)
  I8MM (Integer Matrix Multiply)
  SME (Scalable Matrix Extension)
Pruning
Quantization
Loop Tiling
Notes: Algorithmic optimizations such as quantization and pruning improve efficiency.
Implementation details like loop tiling, reordering, and unrolling enhance performance.
ARM architecture features such as SVE, I8MM, and SME enable specialized optimizations.
Multithreading helps maximize core utilization for parallel computation.

## Slide 15: Bringing It All Together in KleidiAI
What is KleidiAI?
  Open-source library of performance-critical micro-kernels for Arm CPUs
  Designed for easy integration in C/C++ AI/ML frameworks
  Operators are extremely well optimized, written in hand-crafted assembly.
ukernel
  A number of variants each implemented with different datatype/features (I8MM, SVE, …)
  Can be multithreaded to produce a full matrix multiply.
Packing the weight matrix (rhs) for efficient memory access
Run the KleidiAI Matmul ukernel
KleidiAI: https://gitlab.arm.com/kleidi/kleidiai
Notes: KleidiAI is an open-source library of optimized micro-kernels for ARM CPUs.
Designed for integration in C/C++ AI/ML frameworks.
Micro-kernel provides multiple variants with different datatypes like I8MM and SVE.
Supports multithreading for full matrix multiplication.
Example code shows efficient weight matrix packing and execution.

## Slide 16: Summary
Algorithmic optimizations
  Linear quantization reduces model size and improves compute efficiency.
  Network pruning removes redundant parameters to speed up inference.
Implementation techniques
  Loop tiling, reordering, and unrolling optimize matrix multiplication performance.
  Multithreading leverages parallelism for higher throughput.
Arm CPU SIMD technologies
  Neon, SVE, I8MM, and SME provide specialized hardware instructions for faster matrix operations.
Kleidi micro-kernel integration
  Combining these methods with Kleidi micro-kernel yields maximal CPU inference performance.
Notes: Linear quantization reduces model size and improves computational efficiency.
Network pruning eliminates redundant parameters to speed up inference.
Implementation techniques like loop tiling, reordering, and unrolling optimize performance.
Multi-threading allows leveraging CPU parallelism.
ARM CPU SIMD technologies like Neon, SVE, I8MM, and SME provide specialized hardware acceleration.
Combining these methods with KleidiAI yields maximum CPU inference performance.

## Slide 17: Questions and Discussion